## Slide 1: ME 310 Project :
Heat Transfer Equipment Design

## Slide 2: Submitted By :
Md. Farhan (1710035)
Md shahed Hossain sohan (1710043)
abu hanifa (1710044)
Mehedi hasan (1710060)

## Slide 3: Shell & Tube HX with Helical Baffle

## Slide 4: Abstract
In the present study, three-dimensional numerical simulation of shell-and-tube heat exchangers (STHXs) with continuous helical baffle (STHXsHB) is carried out and is performed based on the simulation results.
The STHXs contain 25 tubes inside a 500 mm long and 200 mm diameter shell and mass flow rate of shell-side fluid is varied from .3 kg/s to .4 kg/s. At first, physical and mathematical models are developed and numerically simulated using finite element method (FEM).

## Slide 5: Abstract
For the validation of the computational model, shell-side average nusselt number (Nus) is calculated from the simulation results and compared with the available experimental results. The comparative study shows that STHXsHB has 72-127% higher heat transfer coefficient per unit pressure drop compared to the conventional STHXsSB for the same shell-side mass flow rate. Moreover, STHXsHB has 59-63% lower shell-side pressure drop than STHXsSB.

## Slide 6: Introduction
Heat exchangers are an inseparable part of industries such as power plants, process industries, oil refining and so on. Meanwhile, Shell and Tube Heat Exchangers (STHX) have 40% share apparatus of different industries. So, focusing on this type of heat exchangers to improve the performance has a great importance. Baffles and tube configuring have profound effect on the performance of shell and tube heat exchangers. Common segmental baffles can be referred but they have such problems like: creation of dead zones, decreasing the lifetime of the heat exchanger by creating vibration caused by fluid flow across tube bundle. Researches have been done for different baffle shapes, configurations and tube arrays i.e. triangular, square pitch etc.

## Slide 7: Introduction
Baffles have been used of numerous shapes i.e. segmental, double segmental, helical, segmental-helical, flower shaped etc. In this study, numerical observation has been conducted on shell and tube heat exchanger with helical baffles. These type of baffles are introduced to remove the defects of segmental baffles. Literature review shows that When traditional segmental baffles are used in shell and tube heat exchanger, higher pumping power is often needed to offset higher pressure drop under same heat load. The problems of segmental STHX mentioned above were improved or solved by helical baffles.

## Slide 8: Problem Statement
In this project, a shell and tube heat exchangers’ heating efficiency has been increased for a lower pressure drop than the conventional segmental baffles. In the shell side, hot fluid was entered and cold fluid passed through the tubes. This is a CFD approach.

## Slide 9: Objectives
To design a efficient shell and tube heat exchanger with helical baffle.
To reduce the pressure drop for both shell side and tube side.
To reduce vibration by introducing continuous shell side fluid.

## Slide 10: Hand Calculation Results
 | Shell side (Hot fluid-Water) | Tube side (Cold fluid-Water)
Inlet Temperature | 90C | 15C
Outlet Temperature | 83C | 22C
Dimensions | Shell side (Hot fluid-Water) | Tube side (Cold fluid-Water)
Inner dia, mm | 254,5 | 15.7
Outer dia, mm | 273.1 | 19.05
Nt | 25 | 
Tube orientation | Triangular | 
Pitch, mm | 25.4 | 

## Slide 11: Hand Calculation Results
Dimensions | Shell side (Hot fluid-Water) | Tube side (Cold fluid-Water)
Inner dia, mm | 254,5 | 15.7
Outer dia, mm | 273.1 | 19.05
Nt | 25 | 
Tube orientation | Triangular | 
Pitch, mm | 25.4 | 
Pitch ratio | 1.33 | 
Hydraulic dia, mm | 183 | 15.7
Baffle helix angle | 32.5 | 
Number of turns | 1 | 
Flow type | Turbulent | Turbulent

## Slide 12: Design strategy
Solidworks model
Figure: Helical Baffle

## Slide 13: Design strategy
Solidworks model
Figure: Shell and tube heat exchanger whole and sectional view

## Slide 14: Design Model
Figure : Shell Fluid Temperature Contour

## Slide 15: Design Model
Figure: Temperature Contour (XY plane)

## Slide 16: Design Model
Figure: Tube Fluid Pressure Contour

## Slide 17: Design Model
Figure: Shell Fluid Pressure Contour

## Slide 18: Design Model
Figure: Shell Fluid Velocity Profile

## Slide 19: Design Model
Figure: Shell Fluid Velocity Profile

## Slide 20: Design Model
Figure: Shell Fluid Velocity Profile

## Slide 21: Design Model
Figure: Shell Wall Temperature

## Slide 22: Design Model
Figure: Temperature Contour

## Slide 23: Design Model
Figure: Tube Wall and Baffle Temperature (Isometric View)

## Slide 24: Design Model
Figure: Tube Wall and Baffle Temperature (Front View)

## Slide 25
Output Summary Page 1 Released to the following company: Heat Equipment Designer Mehedi Hasan |  |  |  | 
Xist 7.3.2 2/23/2022 11:26 SN: 46639- SI Units Rating - Horizontal Countercurrent Flow TEMA AES Shell With Single helical Baffles |  |  |  | 
See Data Check Messages. See Runtime Messages. |  |  |  | 
Process Conditions Hot Shellside |  |  | Cold Tubeside | 
Fluid name Water |  |  | water | 
Flow rate (kg/s) 0.3000 |  |  | 1.6500 | 
Inlet/Outlet Y (Wt. frac vap.) 0.0000 0.0000 |  |  | 0.0000 0.0000 | 
Inlet/Outlet T (Deg C) 90.00 77.00 |  |  | 15.00 17.37 | 
Inlet P/Avg (kPa) 0.000 0.000 |  |  | 0.000 0.000 | 
dP/Allow. (kPa) 6.23 70.000 |  |  | 1.958 70.000 | 
Fouling (m2-K/W) 0.000090 |  |  | 0.000090 | 
Exchanger Performance |  |  |  | 
Shell h (W/m2-K) 879.59 |  | Actual U (W/m2-K) 583.48 |  | 
Tube h (W/m2-K) 4421.8 |  | Required U (W/m2-K) 529.23 |  | 
Hot regime (--) Sens. Liquid |  | Duty (MegaWatts) 0.0164 |  | 
Cold regime (--) Sens. Liquid |  | Eff. area (m2) 0.461 |  | 
EMTD (Deg C) 67.2 |  | Overdesign (%) 10.25 |  | 
Shell Geometry |  | Baffle Geometry |  | 
TEMA type (--) AES |  | Baffle type Single Helical |  | 
Shell ID (mm) 200.00 |  | Helix angle (deg) 32.50 |  | 
Series (--) 1 |  | Baffle crossing fraction 0.0694 |  | 
Parallel (--) 1 |  | Central spacing (mm) 25.000 |  | 
Orientation (deg) 0.00 |  | Helical baffle sets (--) 1.0000 |  | 
Tube Geometry |  | Nozzles |  | 
Tube type (--) Plain |  | Shell inlet (mm) 26.645 |  | 
Tube OD (mm) 12.700 |  | Shell outlet (mm) 26.645 |  | 
Length (m) 0.500 |  | Inlet height (mm) 24.909 |  | 
Pitch ratio (--) 1.2500 |  | Outlet height (mm) 24.909 |  | 
Layout (deg) 30 |  | Tube inlet (mm) 52.553 |  | 
Tubecount (--) 25 Tube Pass (--) 1 |  | Tube outlet (mm) 52.553 |  | 
Thermal Resistance, % | Velocities, m/s Min Max Tubeside 0.95 0.95 Crossflow 0.32 0.32 Window -- -- |  |  | 
Shell 66.33 |  |  |  | 
Tube 17.83 |  |  |  | 
Fouling 12.35 |  |  |  | 
Metal 3.49 |  |  |  | 

## Slide 31
Economic consideration:

## Slide 32
Economic consideration:

## Slide 33
Economic consideration:

## Slide 34
Economic consideration:

## Slide 35: Final Results:
 | Shell side - Water | Tube side - Water
Outer Dia, mm | 18 | 12.7
Inner Dia, mm | 200 | 250
Length, mm | 1000 | 1000
Np | 1 | 1
Nt |  | 25

## Slide 36: Conclusion:
In this study, we tried to increase the heat transfer efficiency for a shell and tube heat exchanger adding helical shaped baffles. Our main objective was to increase heat transfer with lower pressure drop. From the calculation and simulation it is clear that the pressure drop was little for both shell fluid and tube fluid. This incurs lower pumping power to flow the fluid through shells and pipes. The helical baffles used here has made the flow more smoother and continuous. As we have simulated for a simplified baffle and tube geometry, there was some mismatch between the result from simulation and software calculation.

## Slide 37: Thank You